2012 T-300k Operating manual

1.	T-300k System features

A.	32—256 grade Gray level，Support software Gamma correction。

B.	Support the rules and special-shaped handle.

C.	8 ports output，one port can support 512-1024 lamp pixels.

D.	On-line (also can SD Card) control, offline control Can be multiple controllers used in combination, the contents of the line control program stored in the SD card.

E.	Compatible with single line or double line chips.

F.	If the controller to the lamps distance can choose photoelectric isolated transmission and as far as several distances of up to 200-300 M

Note: the T-300 K controller offline control, each machine controller must put a SD card.

2012 Edition T-300K controller can only be combined with the new version software LedEdit2012 . Using the old software does not support the new version of the controller, the new version of the controller has been printed the Chinese sign.

2.	Support chips：

| Support chips： | Software code& Controller type | Lamps/(MAX) | NOTE |
| --- | --- | --- | --- |
| LPD6803,D705,1101,6909, 6912 | T-300K-6803 | 8192 | 32 grade gray level |
| LPD8806,LPD8809 | T-300K-8806 | 4096/8192 |  |
| TM1803,TM1804,TM1809,TM1812 | T-300K-TM | 4096/8192 | TM1804&TM1809 Divided into high speed and low speed |
| TM1903，TM1904，TM1909，TM1912 | T-300K-TM19 | 4096/8192 |  |
| UCS6909，UCS6912，UCS7009，UCS5903 | T-300K-UCS32 | 8192 |  |
| UCS1903，UCS1909，UCS1912 | T-300K-UCS256 | 4096/8192 | Divided into high speed and low speed |
| UCS3903 | T-300K-UCS1024 | 4096/8192 |  |
| DMX512 | T-300K-DMX | 1360/4096 | Compatible with standard DMX512 |
| WS2801,WS2803 | T-300K-WS | 4096/8192 |  |
| WS2811 | T-300K-WS2811 | 4096/8192 | Divided into high speed and low speed |
| DS189 | T-300K-DS189 | 4096/8192 |  |
| TLS3001,TLS3002，TLS3008 | T-300K-TLS | 4096/8192 |  |
| P9813 | T-300K-P9813 | 4096/8192 |  |
| SM16715 | T-300K-SM16715 | 4096/8192 | Divided into high speed and low speed |
| SM16716 | T-300K-SM16716 | 4096/8192 |  |
| BS0901,BS0902 | T-300K-0901 | 4096/8192 |  |
| BS0815 | T-300K-0815 | 4096/8192 |  |

NOTE：if chip is 256 grade gray level and Single-line IC choose .When programming choice high speed mode and one interface controls 1024 lamps the play speed can reach 30 frames/s. Double-line IC or single-line IC with low speed , one interface controls 512 lamps the play speed can reach 30 frames/s.

3.	Appearance picture

| Picture 1 | picture 2 |
| --- | --- |

4.The meaning of flag

TTL signal（245 signal）：

| AC IN | Exchange 220V power supply | COM(common port) | GND (ground wire) |
| --- | --- | --- | --- |
| POWER | POWER LIGHT | DAT | Signal |
| STATUS | Status light | CLK | The clock line |
| SD CARD | SD card slot |  |  |

NOTE：According to TTL signal output， Ground of the controller must be connected to the lamp ground.

5.System architecture figure

Note：The IP address of the computer should be set to: 192.168.60.178

6.  wiring diagram

Note：

1.	If the distance between controller and lamps more than 50m we suggest using differential signal transmission control or Photoelectric isolated signal transmission control，please read the manual carefully. Signal lines must be a cable，the best is Super five kinds of cable.

7. Application scope

LED digital tube,、LED point light source、the exterior light and a module、 pixel screen (dazzle colour screens)、 high power DMX lighting.

8.Specific parameters：

Memory card：

Type：SD card（if controlling so many lamps it is best to use the high-speed SD card.）

Capacity：128MB—2GB

Format：FAT

Store file：*.led

Physical parameters：

Working temperature ：-30℃—85℃

Weight：1.35KG

Working voltage：AC220V

Working power：8W

Size：L270mm�W180mm�H55mm

Signal port：3pin connect port

NOTE: T-300K Support online download the effect-file to SD card.

Before copy files to SD card ，The SD card must be formatted as FAT format.

The SD card in controller can not be hot-swappable, plug the SD card every time, you must first disconnect the power supply

9. Differential signal transmission control

1.Purpose：

For many big engineering ,the distance between lamps and controller more than 50m and less than 200m.

2、details

built-in Signal transmitter——> signal transmission Repeaters——> signal transmission receiver。

3、Appearance picture

4、Mode of connection：

5、Attention：

the distance， between controller and transmission Repeaters、between transmission Repeaters and transmission Repeaters 、between transmission Repeaters and signal transmission receiver  can’t more than 50m。The maximum distance between controller and signal transmission receiver is 200m。

10. Trouble shooting

Question 1: controller after electrify, indicator light is normal, but the lamps no effect change

Answer: the reasons for this are the following:

(1) Please check lamps signal and controller have correct connection.

(2) If it is meet TTL signal, lamps and lanterns and controller must altogether, namely the lamps GND (ground) to the GND and controller (ground) got together.

(3) Please check the effect file of SD card ，the selected models whether current lamps and used the chip consistent.

Question2

After power, the T-300k   ERROR indicator has been flashing without display output

answer：The ERROR indicator has been flashing means the controller did not read the card correctly, possible problems:

①SD card is empty, with no effect file.

②The effect file in the SD card and the controller model are not match, please choose correct controller model in LedEdit and then re-create the effect file *led.

③SD card did not format to FAT before copy effect files.

④Please check the supply power voltage, the controller can be individually powered to exclude power reasons

⑤Changing the SD card and then test to exclude the possibility of a bad SD card